## Slide 1: Update on POLA-01 measurements in Catania
14/02/2019
Chiara Pinto, Francesco Riggi, Paola La Rocca

## Slide 2: Outline
Summary on POLA-01 – CATA-01 coincidence measurements
Possible use of these measurements to monitor civil structures stability
MC simulations and optimization of relative position between detectors

## Slide 3: Measurements
Measure 1 – outside the acceptance interval of CATA-01, in order to detect two independent muons coming from the same shower. About 13 days acquisition time.
Measure 2 – inside the acceptance interval of CATA-01, in order to detect also muons passing through both detectors. Detectors geometry select a narrow acceptance cone (POLA-01: 40 cm x 60 cm). About 47 days acquisition time.

## Slide 4
5,4 m
7,6 m
CATA-01 → floor -1
POLA-01 → floor 3
POLA-01
CATA-01
Geometrical disposition of the two detectors in Catania Physics department.
15 m
floor 3
floor -1
CATA-01
POLA-01

## Slide 5: Track selection
Coincidence window
¦(Δt + (t-int(t)) ∙ 2500 -1500) – 140¦ < 600 ns
Quality cuts
χ2 < 10
-2 ns < ToF < 10 ns
Number of satellites POLA-01 ≥ 3
Number of satellites CATA-01 ≥ 3
Number of tracks POLA-01 = 1
Number of tracks CATA-01 = 1
Measurements OUTSIDE CATA-01 acceptance cone: 3 days data taking.
Measurements INSIDE CATA-01 acceptance cone: 13 days data taking.
Corrected time difference spectrum

## Slide 6: Theta distribution
On the left panel the background due to independent muons is shown.
On the right there is a peak in a selected region of θ, corresponding to muons passing through both detectors, superimposed on the background.
< θ > | Δ<θ>
31.03° | 0.05°
POLA-01 outside CATA-01 acceptance
POLA-01 inside CATA-01 acceptance

## Slide 7: Phi distribution
As before, for the φ distribution.
< φ > | Δ<φ>
216.43° | 0.20°
POLA-01 outside CATA-01 acceptance
POLA-01 inside CATA-01 acceptance

## Slide 8: Monitoring of civil structures stability
IDEA → using a tracking detector (EEE telescope) and an additional detector (e.g. a scintillator) to test the civil structures stability on a long time scale.
This tool can monitor small (mm) shifts of parts of the structure over long time periods.
→ No need of visibility or empty spaces (VS optical systems)
Performances of the method depend on the capability of the main tracking detector, geometry and position of the additional detectors , measurement stability, acquisition time, ...

## Slide 9: Measurements
Four sets of measurements:
Reference -> 0 cm
First shift -> 20 cm
Second shift -> 10 cm
Third shift -> 5 cm
x [cm] 20 10 5 0
POLA-01
POLA-01

## Slide 10: Theta variation per day
Extracting θ centroids day by day one can see that in average there is a shift.
Notes: blue points (20 cm shift) are higher than red points (reference position), and green points (10 cm shift) are in an intermediate position between red and blue points.

## Slide 11: 20 cm shift
x [cm] | < θ > ± Δ<θ> | < φ > ± Δ<φ>
0 | 31.03° ± 0.05° | 216.43° ± 0.20°
+20 | 31.45° ± 0.06° | 216.23° ± 0.32°
POLA-01 inside CATA-01 acceptance
POLA-01 inside CATA-01 acceptance

## Slide 12: 10 cm shift
x [cm] | < θ > ± Δ<θ> | < φ > ± Δ<φ>
0 | 31.03° ± 0.05° | 216.43° ± 0.20°
+10 | 31.36° ± 0.08° | 216.15° ± 0.29°
POLA-01 inside CATA-01 acceptance
POLA-01 inside CATA-01 acceptance

## Slide 13: 5 cm shift
POLA-01 inside CATA-01 acceptance
POLA-01 inside CATA-01 acceptance
x [cm] | < θ > ± Δ<θ> | < φ > ± Δ<φ>
0 | 31.03° ± 0.05° | 216.43° ± 0.20°
+5 | 31.36° ± 0.08° | 216.15° ± 0.29°

## Slide 14: Distribution of average direction in space
Estimation of the average direction in space, summing on all the tracks, in 3 configurations (5 cm, 10 cm, 20 cm).
Relative distance | Relative angle shift
20 cm | 0.44°
10 cm | 0.24°
5 cm | 0.31°
5 cm measurement has a very short statistics – just 4 days
Mean values for θ and φ angles, estimated with a gaussian fit.
Gaussian fit |  | 
x [cm] | < θ > ± Δ<θ> | < φ > ± Δ<φ>
0 | 31.03° ± 0.05° | 216.39° ± 0.16°
+5 | 31.18° ± 0.07° | 215.88° ± 0.33°
+10 | 31.36° ± 0.08° | 215.98° ± 0.30°
+20 | 31.45° ± 0.06° | 215,67° ± 0.20°

## Slide 15
CATA-01 → floor -1
POLA-01 → floor 3
POLA-01
CATA-01
Effect of relative position
Performances of the method depend on the capability of the main tracking detector, geometry and position of the additional detectors , measurement stability, acquisition time, ...
So, we moved POLA-01 in a different position, in order to estimate the effect of the relative position.
2,5 m

## Slide 16: Closer to the vertical position
POLA-01 inside CATA-01 acceptance
POLA-01 inside CATA-01 acceptance
x [cm] | < θ > ± Δ<θ> | < φ > ± Δ<φ>
vertical | 13.32° ± 0.02° | 87.14° ± 0.17°

## Slide 17: Statistics
Relative horizontal distance between detectors | Acquisition time | # events
9,3 m | ~ 7 ∙ 105 s | 757
2,5 m | ~ 6 ∙ 105 s | 4305
Statistics increased of a factor ~ 7, in agreement with MC simulations.
2,5 m
9,3 m
Simulations Experimental results
Relative distance | Relative angle shift
20 cm | 0.44°
10 cm | 0.24°
5 cm | 0.31°

## Slide 18: Conclusions and outlook
Present sensitivity of the method may be roughly estimated of the order of few cm for a data taking period of 1 week
Proper optimization of relative position can increase statistics
Monte Carlo simulations in progress to better understand the results and improve operational conditions
Paper in preparation