## Slide 1: Test of new ECO-Gas Mixtures for the MRPC of the EEE project
Marina Trimarchi
on behalf of the EEE collaboration
Museo Storico della Fisica e Centro Studi e Ricerche “Enrico Fermi”, Roma
Dipartimento MIFT – Università degli Studi di Messina
INFN – Sezione di Catania

## Slide 2: The EEE Project
Extreme Energy Events
  Centro Fermi, INFN, CERN & MIUR
Study of Cosmic rays and related phenomena
A sinchronous sparse network of 59 tracking detectors installed in Italian High Schools
  Each made of 3 Multigap Resistive Plate Chamber detector
  More than 10° in latitude and 11° in longitude
    More than 3 x 105 km2
Three MRPC providing the impact coordinates of incoming muons
  The reconstruction of their tracks, with high efficiency and good angular resolution
Detectors operate in avalanche mode
  Characteristics similar to the ones built for the ALICE TOF array

## Slide 3: The Global Warming Potential Reduction Problem
GWP measures the greenhouse effect of a gas
  Normalized to CO2 (GWP=1)
Recent EU restrictions on GWP  (max = 150)
EEE MRPC R134a(98%) + SF6(2%)
  GWP = 1900
Extensive tests of several gas mixtures with cosmic muons detected by one of the telescopes installed at CERN
  Detection efficiency, chamber current, cluster size as a function of the applied HV
Tested Gas Mixtures
Pure R1234ze (GWP=6) (tetrafluoropropene - C3H2F4)
R1234ze(90%) + CO2(10%)
R1234ze(80%) + CO2(20%)
R1234ze(50%) + CO2(50%)
R1234ze(95%) + SF6(5%)
R1234ze(98%) + SF6(2%)
R1234ze(99%) + SF6(1%)
CO2(100%)
CO2(98%) + SF6(2%)

## Slide 4: Test performed
CERN-01 chambers (operating with the nominal mixture)
  Provide the trigger for the event acquisition
Good events: muons crossing the three chambers
Events readout
  Two bottom-most chambers+ chamber under test
    Operating with the new mixtures, provided by the external mixer

## Slide 5: Pure tetrafluoropropene (R1234ze) (GWP=6)
preliminary
Higher HV setting point!!!
Streamer percentage below 5%
preliminary
preliminary
Stable cluster size & low dark current

## Slide 6: R1234ze + CO2 (GWP=1)
Streamer percentage increases
preliminary
Lower HV setting point
preliminary
preliminary
High dark current & high cluster size

## Slide 7: R1234ze+SF6
High HV setting point
preliminary
Satisfactory streamer percentage
preliminary
Noise highly suppressed but SF6 % too high!!

## Slide 8: CO2-based mixtures
Very low HV setting point…
preliminary
Efficiency too low!!!
preliminary
preliminary
Very noisy configuration!!

## Slide 9: Conclusions
preliminary
Future Plans
R134a+CO2(5,10,20,50%)
Ar+CO2(3,5,10,20%)
Ar+SF6(1,2%)
N2+CO2(3,5,10,20%)
N2+SF6(1,2%)
Most Promising configurations
Pure R1234ze
R1234ze(50%) + CO2(50%)
preliminary