## Slide 1: Performance of MRPC telescopes of the EEE Project
E. Bossini, C. Cicalò, D. De Gruttola,
I. Gnesi, M. Garbini, S. Grazzi, S.M. Panetta
EEE meeting
01/06/2016

## Slide 2
time resolution (almost final)
spatial resolution (almost final)
efficiency (ongoing measurement)
comparison with 3 indipendent analysis (consistent)
writing (well advanced)
Status
EEE meeting
01/06/2016
2

## Slide 3
DThit = (TH_bot + TH_top)/2 - TH_mid
sT = √3/2sDT ~ 207 ps
time slewing correction to be applied (soon)
Time resolution
no selection on events w/o clusters
cut on reconstructed tracks c2 < 10
strip by strip calibration applied
result obtained on TORI-03 (same clock distributed to both TDCs)
available results from telescopes with different clocks on TDCs
results recently presented at a conference (RPC 2016)
EEE meeting
01/06/2016
3

## Slide 4
DX = (Xbot + Xtop)/2 – Xmid
sX = √3/2sDX ~ 1.9 cm
two contributions are visible  to be
understood
two gauss ditributions used for the fit
using only one gauss sX = 2.05 cm
sXexp ~ vsignal*(DTlef2+DTright2 )2 ~ 0.68 cm
(TDC resolution 100 ps  vsignal ~ 15.6 cm/ns)
Spatial resolution (long side)
no selection on events w/o clusters
cut on reconstructed tracks c2 < 10
strip by strip calibration applied
result obtained on TORI-03 (same clock distributed to both TDCs)
available results from telescopes with different clocks on TDCs
results recently presented at a conference (RPC 2016)
EEE meeting
01/06/2016
4

## Slide 5
Spatial resolution (short side)
DY = (Ybot + Ytop)/2 – Ymid
sY = √3/2sDY ~ 1 cm
sYexp ~ pitch/√12 ~ 0.92 cm
(pitch 3,2 cm)
study fit procedure in detail (triangular function?)
no selection on events w/o clusters
cut on reconstructed tracks c2 < 10
strip by strip calibration applied
result obtained on TORI-03 (same clock distributed to both TDCs)
available results from telescopes with different clocks on TDCs
results recently presented at a conference (RPC 2016)
EEE meeting
01/06/2016
5

## Slide 6
MC spatial distribution
simulation ready  to be optimized
1 hit and 2 angles are simulated at the moment
events with 2 hits to be added
bin width 8 mm
bin width 4 mm
EEE meeting
01/06/2016
6

## Slide 7
Efficiency
measurement ongoing on TORI-03
external trigger used (two 15x15 cm2 scintillators)
5 areas on the chambers are scanned
results of eff vs HV performed after Run 2 can be included
EEE meeting
01/06/2016
7

## Slide 8
Efficiency vs HV for a single MRP Chamber (Triggered by scintillators) Efficiency plateau100%
TEST BEAM at CERN
spatial resolution along strips 8 mm
TDCs 25ps bins , scintillators system time resolution 30 ps
Results from test beam (2006)
sT ~ 141 ps in the center of the strip
with time slewing correction
and scintillators time resolution
sT ~ 94 ps
EEE meeting
01/06/2016
8

## Slide 9
Comparison with indipendent analysis
3 indipendent analysis:
results are compatible with analysis from “performance working group”
EEE meeting
01/06/2016
9
recent analysis from degree students in Pisa
old analysis for degree in 2008 in Bologna
recent analysis on multitrack events from F. Nozzoli

## Slide 10
Bologna
EEE meeting
01/06/2016
10
analysis done in Bologna in 2008 (graduate student)
sx=0.9 cm
sy=2.1 cm
sy=1.3 cm
vertical tracks

## Slide 11
EEE meeting
01/06/2016
11
Pisa
raw alignment with the box distribution
track cuts applied after the alignment (1 hit/chamber, c2/d.o.f. < 4)
align the middle chamber with the residual distribution
iterate
re-scan all events with the new calibration
hit position obtained by correcting the offset of the box distribution
hit raw time of the middle chamber centered wrt the external chambers
similar results for spatial resolution
(sx~ 1.4 cm, sy ~ 1.2 cm)
very good time resolution
analysis done by graduate students

## Slide 12
Multitrack events
EEE meeting
01/06/2016
12
residual x
residual y
time residual
similar results on SAVO-02 and FRAS-02
SAVO-01
analysis by F. Nozzoli and recently presented at the reco&analysis meeting

## Slide 13
Paper
EEE meeting
01/06/2016
13

## Slide 14
Paper
introduction and description of the setup done
(to be revised)
EEE meeting
01/06/2016
14

## Slide 15
Paper
section on
strategy and
results well
advanced
EEE meeting
01/06/2016
15
figures to be changed

## Slide 16
Paper
section on
strategy and
results well
advanced
EEE meeting
01/06/2016
16

## Slide 17
Paper
comparison with results from beam test to be written
EEE meeting
01/06/2016
17

## Slide 18
analysis  almost final
paper writing  advanced status
TOT and slewing correction to be included (ongoing)
Conclusions
EEE meeting
01/06/2016
18