## Slide 1
Fisica e medicina: radionuclidi e radiofarmaci
gaia.pupillo@lnl.infn.it
Notes: 15 min talk + 5 min domande (20 min)
ISOLPHARM + LARAMED + INFN e Prospettive
Intro 3 min
ISOLPHARM 5 min
LARAMED 10 min
Finale 2 min , con prospettive

## Slide 2
Why am I here?
Please ask questions!

## Slide 3
The role of physics in medicine.. a long love story
1895 Röntgen
X – ray discovery
1896 Becquerel
Radioactivity discovery
1897 Rutherford
α and β discovery
1900-1908
M.me Curie
Ra and Po discovery
(both more radioactive than uranium)
Marie Skłodowska was born in Warsaw, Poland, to a family of teachers who believed strongly in education. She moved to Paris to continue her studies and there met Pierre Curie, who became both her husband and colleague in the field of radioactivity. The couple later shared the 1903 Nobel Prize in Physics. Marie was widowed in 1906, but continued the couple's work and went on to become the first person ever to be awarded two Nobel Prizes. During World War I, Curie organized mobile X-ray teams. The Curies' daughter, Irene, was also jointly awarded the Nobel Prize in Chemistry alongside her husband, Frederic Joliot.

## Slide 4
Something you may not know.. Crowdfunding!
M.me Curie was a great researcher, Nobel prize in Physics (1903) and in Chemistry (1911) ..
.. But it is not well known how active she was also in the application of radiation to medicine.
During 1° world war, she developed the Petites Curie, cars equipped with x-ray systems able to make diagnosis for injured soldiers. The Petites Curie were equipped with an x-ray syistem and a dark chamber.
To develop them, M.me Curie get the money with a «crowfunding» system and trained many nurses to drive and use the Petites Curie.
M.me Curie during I World War driving a Petit-Curie
It was estimated that the total number of injured soldiers that received x-ray exams during the war was more than 1 million!

## Slide 5
How do x-rays work?

## Slide 6
When are x-rays useful?

## Slide 7
Are you able to say if he is alive?
Physicians need a different tool to investigate the biological behaviour of the cells

## Slide 8
Radionuclides
Numero di protoni Z
Numero di neutroni N
Beta +
Beta -
Alfa
Fission
Stable ~ 279
Radioactive ~ 5000

## Slide 9
Radionuclides

## Slide 10
Radionuclides
Half-life
12.32 years (Y)
Emitted radiation:
Beta-

## Slide 11
Interaction of radiation and matter
Alpha
Beta
Gamma
Paper
Al
Pb
Neutron
H2O

## Slide 12
Radionuclides and radiopharmaceuticals
Radionuclide with suitable physical and chemical properties
Capacity to localize the radionuclide in the specific, desired biological target

## Slide 13
Radionuclides and radiopharmaceuticals
imaging

## Slide 14
How do radiopharmaceuticals work?
Useful decay radiation for imaging: photon (γ) or positron (β+)

## Slide 15
Are you able to say what is this?

## Slide 16
How does SPECT imaging work?
Useful decay radiation for SPECT imaging: photon (γ)
SPECT_Single Photon Emission Tomography

## Slide 17
Cardiac SPECT imaging

## Slide 18
How does PET imaging work?
Useful decay radiation for PET imaging: positron (β+)
PET_Positron Emission Tomography
νe
Beta+
gamma
gamma

## Slide 19
Multi-modality imaging
PET-CT
+
=
Morphology + Biochemistry = Localization of the disease
SPECT-CT
PET-MRI

## Slide 20
How does therapy with radiopharmceuticals work?
Useful decay radiation for theraphy: alpha (α), beta (β-) and Auger e-

## Slide 21
How does therapy with radiopharmceuticals work?
Useful decay radiation for theraphy: alpha (α), beta (β-) and Auger e-
Elettroni (β-)
Alfa (α)

## Slide 22
Radionuclides and radiopharmaceuticals
therapy
THERAPY

## Slide 23
Radionuclides and radiopharmaceuticals
Selection of patients!

## Slide 24
It’s very important to have a variety of medical radionuclides
Radionuclides and radiopharmaceuticals

## Slide 25
Medical radionuclides production
Production routes
Direct:
Generator:
For example 99Mo/99mTc, …
For example 18F, 11C , 131I, …

## Slide 26
Medical radionuclides production
Nuclear reactors
Particle accelerators
Medical cyclotron at the Sacro Cuore Don Calabria hospital (Protons 19 MeV)

## Slide 27
The SPES project
SPES-α
The cyclotron and related infrastructure.
SPES-β
The ISOL facility and the acceleration of neutron-rich unstable nuclei.
SPES-γ
The production of radionuclides for applications.
SPES-δ
The multidisciplinary neutron sources.

## Slide 28
https://isolpharm.pd.infn.it/web/
https://www.lnl.infn.it/en/spes-laramed-range
SPES-γ
The production of radionuclides for applications
ISOL technique
A. Andrighetto
Resp. ISOLPHARM
Direct activation
J. Esposito
Resp. LARAMED
SPES-γ

## Slide 29: ISOLPHARM: the Method
ISOLPHARM method is capable of selecting and isolating a
SINGLE RADIO-ISOTOPE
+ high specific activity
+ radionuclidic purity
The ISOLPHARM Method is an INFN Patent

## Slide 30
Cyclotron Radioisotope production
Target
Irradiation
Radioisotope of interest
Contaminants
Dissolution
Extraction/
separation
Purification
Radiochemical processing
Quality controls
Pure radioisotope
Radio-
pharmaceutical preparation
Labelling
Nuclear physics
Target activation
LARAMED: Production steps

## Slide 31
LARAMED facility
Pass box
Central corridor
Hot Cell
RILAB Radiochemistry labs
Bunker A9c
Cyclotron
RILAB chemistry / targetry labs

## Slide 32
LARAMED projects & network
64Cu
67Cu
99mTc
47Sc
43Sc
44mSc
155Tb
161Tb
152Tb
149Tb
52Mn

## Slide 33
Target manufacturing
Cyclotron irradiation
Radiochemistry processing
Radiopharmaceuticals, QC & imaging
100Mo recovery
APOTEMA
TECHN-OSP
Direct production exploiting the
100Mo(p,2n)99mTc
reaction
99mTc direct production cycle
CRP on 99Mo/99mTc suppy (2011/2015)
Closed-loop technology developed at LNL: recovery of costly target material
99mTc
International Patent
n° WO2019053570

## Slide 34: 52Cr target manufacturing technology by SPS
52Mn and the METRICS project
Development of 52/51Mn/Cr efficient separation
52Mn
52Mn | Eβ+ (avg) 250 keV | PET
51Mn | Eβ+ (avg) 960 keV | 
Mn2+ | Paramgnetic properties | MRI contrast agent

## Slide 35
67Cu as theranostic agent
CRP on 67Cu, 47Sc, 186Re (2016/2020)
64Cu
67Cu
68Zn(p,2p)67Cu
68Zn(p,x)64Cu
10
60
20
Most used targets for 67Cu production: 68Zn
COME project
INFN-CSN3 2016
67Cu: 2.58 d
Mean β- energy: 141 keV (100%)
Main γ-ray 184 keV (48.7%)
 SPECT
64Cu: 12.7 h
Mean β- energy: 191 keV (38.5%)
Mean β+ energy: 278 keV (17.49%)
 PET

## Slide 36
67Cu cross section measurements
Scheme of a typical stacked-foils target
Stacked-foils target assembly
γ-spectrometry
Enriched 70Zn targets produced at LNL by lamination
Beam setting with alumina
Irradiation runs on the AX3 beam-line
Target disassembly
Radiochemistry
Data analysis

## Slide 37
γ-spectrometry @ Arronax facility
Before radiochemical separation
After radiochemical separation
xCu-xx-0cm
xGa-xx-0cm
xZn-xx-0cm
MIX-xx-19cm
Activity
measured
Correction for the decay during the time between the end of irradiation and the start of the measurement with HPGe
Correction for the decay during the irradiation
Correction for the decay during the measurement with HPGe
Activity at the End of Instantaneous Bombardment (EOIB)
HPGe detector

## Slide 38
Results

## Slide 39
67Cu as theranostic agent
G. Pupillo, L. Mou et al., Production of 67Cu by enriched 70Zn targets…, Radiochim. Acta 108 (8) 2020

## Slide 40
67Cu as theranostic agent
67Cu/64Cu ratio favourable from 70Zn target above 56 MeV
a.d.u.
Cross section ratio 67Cu/64Cu
International Patent
n° WO 2019/220224 A1
November 2019
“A method and a target for the production of 67Cu”
Mou, Pupillo, Martini, Pasquali

## Slide 41
CUPRUM_TTD (2023-2025)

## Slide 42
STarDiS: Solid Target Dissolution System
Module’s motor
Vial
Mounting rods
Target holder
Module’s heater
AIM: Development of a solid target dissolution system integrable on automatic commercial modules for radiopharmaceuticals synthesis
A complete solution for processing, separation, purification and radiolabelling within a single cassette-based module

## Slide 43
47Sc as theranostic agent
CRP on 67Cu, 47Sc, 186Re (2016/2020)
The limiting factor for clinical and preclinical studies is the lack of 47Sc availability
PASTA project
INFN-CSN5
2017-2018
REMIX project
INFN-CSN5
2021-2023
47Sc
43Sc
44mSc
155Tb
161Tb
152Tb
149Tb
Sc-47 3.3492 d | γ-ray [keV] | γ-ray [%] | β- energy [keV] | β- int [%] | Auger e-[keV] | Auger e- [%]
β- : 100 % | 159.381 | 68.3 | 142.6 | 1.11 | 0.42 | 0.461
(Ti-47) |  |  | 203.9 | 31.6 | 4.0 | 0.215
 |  |  |  |  | 154.415 | 0.277
SPECT
Mean β- : 162 keV
THERAPY
APHRODITE project on 155Tb
MUR, PRIN PNRR (2024-2025)

## Slide 44
WP1. Production & target characterization
Sara Cisternino (INFN-LNL & UniPD)
WP2. XS measurements 49Ti,50Ti
Liliana Mou (INFN-LNL)
WP3. XS measurements natDy,159Tb, natEu
Simone Manenti (UniMI & INFN-MI)
WP4. Nuclear codes (TALYS, EMPIRE, FLUKA)
Luciano Canton (INFN-Padova)
Andrea Fontana (INFN-Pavia)
WP5. Dosimetric calculations
Laura De Nardo (UniPD & INFN-PD)
Laura Melendez-Alafort (IOV)
WP6. 155Tb TTY production
@ SCDC hospital
Petra Martini (UniFE & INFN-FE)
WP7. Devices for INFN-LNL beam-line
Gabriele Sciacca (INFN-LNL & UniPD)

## Slide 45
Many medical radionuclides of interest!
Young team of researchers with different expertise
(targetry, nuclear physics, engineering, radiochemistry, etc.)
Wide national & international network of collaborations +
High potential impact exploiting both ISOL and DIRECT production @ SPES
Possibility to have a off-line mass-separator for medical radionuclides production

## Slide 46
Thanks for the attention!
gaia.pupillo@lnl.infn.it