## Slide 1: Performance of MRPC telescopes of the EEE Project
E. Bossini, C. Cicalò, D. De Gruttola,
I. Gnesi, M. Garbini, S. Grazzi, M.P. Panetta
EEE meeting
22/03/2017

## Slide 2
beta ditributions for all telescopes  almost done for all telescopes
trending for HV and currents  ongoing
duty cycle by trending the rate  ongoing
multiplicity (hits and clusters) distributions  ongoing
c2  ongoing
time-of-flight  ongoing
other trending variables (see starting from slide 5)
time resolution (shown here)
spatial resolution
Status
EEE meeting
2
time slewing correction applied
~20% improvement
offset to be addressed in some telescopes
time slewing correction to be applied
22/03/2017

## Slide 3
TOT – time slewing correction
EEE meeting
3
22/03/2017
middle chamber of TORI-02 as an example
before correction
after correction
the correction works
offset to be understood

## Slide 4
TOT – time slewing correction
EEE meeting
4
22/03/2017
TORI-02
BOLO-03
TORI-02
~20% improvement by applying time slewing correction
value obtained with RMS - fit has to be done
BOLO-03
~5% improvement by applying time slewing correction
worst time resolution wrt other telescopes (not shown here)
value obtained with RMS - fit has to be done
TOT correction to be refined and applied to other telescopes (at the moment results are available
from TORI-02 TORI-03 PISA-01 BOLO-01 BOLO-03)
offset to be studied
more details on the analysis at the next meeting (once it will be refined)

## Slide 5
Study of the long term stability of the array
EEE meeting
5
22/03/2017
Goal: monitor of the interesting parameter for all the telescope during long period
now we are extrapolating:
track rate
reconstruction efficiency (event with candidate tracks/triggered events)
trigger rate
average time of flight
average multiplicity (both single chamber and global)
average number of tracks
number of satellites seen
more can be added…suggestions?
period currently analyzed: from September 2016 up to yesterday (ongoing also for run 1 and run 2)
method:
data are extrapolated from the fist run acquired every N days (N set to 1 in the next slides)
check on file  more than 1K events
if telescope was not online a value of zero is put in the graphs

## Slide 6
Good candidate track rate stability
EEE meeting
6
22/03/2017
No data found
(not trasmitted or
short run)
Days from 1-09-2016
Rate [Hz]
Run 3
Commisioning
Run 3
CAGL-02 as an example

## Slide 7
Poor candidate track rate stability
EEE meeting
7
22/03/2017
CAGL-01 as an example
Days from 1-09-2016
Rate [Hz]

## Slide 8
GPS monitoring
EEE meeting
8
22/03/2017
CAGL-02 as an example
Days from 1-09-2016
In the DAQ if satellites >= 7, the value is fixed to 7 (only 3 bits available)

## Slide 9
CAGL-02 all data
EEE meeting
9
22/03/2017
room for other variables!

## Slide 10
EEE meeting
10
22/03/2017
Summary
several trending plots available
need to find a consistent way to present them
more plots available at the next meeting
time and spatial resolution ready (including time slewing correction, to be refined)