## Slide 1: New EEE Weather Station development
EEE Collaboration Meeting, 22/3/2017

## Slide 2: Oregon Scientific WMR88
Price: ~ 150€
All EEE telescopes use this WS
Proprietary Software
Several sensors, we use only pressure and temperature (internal and external).
VWS write a CSV file (read by DAQ at the beginning of each run).
This model is no longer in production.

## Slide 3: Oregon Scientific WMR89
Price: ~ 150€
Proprietary Software
Same look of WMR88
WMR89 has a data logger for 7 days: driven via that virtual serial port; does not support VWS (probably not even in the future);
I had a test sample for a week: data transfer works only with queries by an interface; you get an excel file.

## Slide 4: We have to move on a different weather station
Continue to use Virtual Weather Station
Develop a new EEE Weather Station
Probably overkilling for our needs

## Slide 5: The purpose of the working group
Develop an EEE Weather Station with three sensors:
  Pressure
  Internal temperature
  External temperature (two solutions: RF sensor or wired sensor, so schools will be able to chose what they prefer).
Determine good practices to improve installation (Weather Instrument Shelter howto)

## Slide 6: Steps
Determine the list of platforms to try (arduino, stm32, NI).
Determine which sensors to use (Ivan Gnesi is in contact with INRIM) and how to calibrate sensors.
Choose the RF module
Build and test the EEE Weather Station

## Slide 7: Possible platforms
NI USB-6000

## Slide 8: Example: Arduino Weather Station
Prices (one unit):
  Microcontroller Arduino: 20 €
  Thermistor MCP9808: 5 €
  Pressure/T/Humidity Bosch BME280: 19 €
Can be assembled by students !!
Full control of the software
Much better sensors than than Oregon Scientific

## Slide 9: Oregon Scientific WMR88 Specs
Barometer:
  Measuring range: 700 – 1050mb/hPa
  Accuracy: +/- 7 mb/hPa
Indoor Temperature
  Operating range: 0°C to 50°C
  Accuracy: 0°C - 40°C: +/- 1°C; 40°C - 50°C: +/- 2°C
Relative Humidity
  Operating range: 25% to 90%
  Accuracy : +/- 7%
Outdoor Temperature
  Operating range: -30°C to 60°C
  Accuracy: not specified

## Slide 10: New sensors (example)

## Slide 11: Bosch BME280 and Microchip MCP9808
Barometer BME280:
  Measuring range: 300...1100 mb/hPa
  Accuracy: < +/- 1 mb/hPa (RMS Noise 0.2 Pa, equiv. to 1.7 cm; Offset temperature coefficient ±1.5 Pa/K, equiv. to ±12.6 cm at 1 °C temperature change )
Indoor Temperature
  Operating range: -40 +85 °C
  Accuracy: < +/- 1°C
Relative Humidity
  Operating range: 0% to 100%
  Accuracy : +/- 3%
Outdoor Temperature
  Operating range: -40°C +125°C
  Accuracy: tipical 0.25°C (from -20 to 100 C); 0.0625°C resolution