## Slide 1
E. Bossini, C. Cicalò, D. De Gruttola,
I. Gnesi, M. Garbini, S. Grazzi, M.P. Panetta
EEE meeting
26/04/2017
Performance of MRPC telescopes of the EEE Project

## Slide 2
time slewing correction applied
st < 200 ps
a few results to be reviewed (too high st)
some big contribution outside the peak (most likely related to clock)
many telescopes show an offset in the Dt distribution
some examples in the next slides (data from Run 3)
Status
EEE meeting
26/04/2017
2

## Slide 3
ALTA-01
EEE meeting
3
st = 214 ps
st = 270 ps
26/04/2017

## Slide 4
BOLO-01
EEE meeting
4
st < 255 ps
st < 342 ps
st = 209 ps
st = 280 ps
26/04/2017

## Slide 5
BARI-01
EEE meeting
5
st = 263 ps
st = 309 ps
26/04/2017

## Slide 6
TORI-01
EEE meeting
6
st = 192 ps
st = 247 ps
26/04/2017

## Slide 7
BOLO-03
EEE meeting
7
st = 178 ps
st = 231 ps
26/04/2017

## Slide 8
BOLO-03 (log y scale)
EEE meeting
8
whole Run 3
Nov 2016
Dec 2016
Jan 2017
no clock card here
no clock card here
in part of this period
clock card ok
but what is the other peak? 
 trigger arriving at the next clock?
26/04/2017

## Slide 9
TORI-03 (log y scale)
EEE meeting
9
clock card ok
but what is the other peak? 
 trigger arriving at the next clock?
whole Run 3
26/04/2017

## Slide 10
time slewing improves time res of about 20%
different values to be understood
offsets to be understood
Status
EEE meeting
10
ALTA01 offset
ANCO01 forse bad clock
AREZ01 ok
BARI01 ok
BOLO01 ok
BOLO02 small offset
BOLO03 ok
BOLO04 small offset
CAGL01 small offset
CAGL02 forse bad clock
CAGL03 forse bad clock
CATA01 ok
CATA02 ok
CATZ01 ok
CERN01 small offset
CERN02 forse bad clock
GROS01 small offset
GROS02 forse bad clock
LAQU01 small offset
LAQU02 forse bad clock
LECC01 small offset
LECC02 small offset
LODI01 small offset
LODI02 small offset
PATE01 small offset
PISA01 offset
REGG01 forse bad clock
SALE01 forse bad clock
SALE02 forse bad clock
SAVO01 ok
SAVO02
SAVO03 small offset
TERA01 small offset
TORI01 offset
TORI03 small offset
TORI04 ok
TRAP01 small offset
TREV01 ok
TRIN01 ok
VIAR01 offset
VIAR02 forse bad clock
this table is not final
(to be studied in different periods)
26/04/2017

## Slide 11
data from Run 2 and Run 3
stability garanteed for a few telescopes in the same period
possibility to chose different shorter periods in order to include other telescopes
need to think to a clever way to plot stops in the acquisition
Trending plots
EEE meeting
26/04/2017
11

## Slide 12
Trending plots
EEE meeting
26/04/2017
12

## Slide 13
Trending plots
EEE meeting
26/04/2017
13

## Slide 14
Trending plots
EEE meeting
26/04/2017
14

## Slide 15
Trending plots
EEE meeting
26/04/2017
15

## Slide 16
Trending plots
EEE meeting
26/04/2017
16

## Slide 17
Trending plots
EEE meeting
26/04/2017
17

## Slide 18
Trending plots
EEE meeting
26/04/2017
18

## Slide 19
Trending plots
EEE meeting
26/04/2017
19

## Slide 20
Trending plots
EEE meeting
26/04/2017
20

## Slide 21
Trending plots
EEE meeting
26/04/2017
21

## Slide 22
Beta distributions
EEE meeting
26/04/2017
22
TORI-03
SAVO-02

## Slide 23
Beta distributions
EEE meeting
26/04/2017
23
TRAP-01
in general we need to fit the b and 1/b distributions with two gaussians

## Slide 24
data from Run 2 and Run 3 provide good data for the paper
still room for improvements for time and spatial resolution
need to decide a policy to better show trending plots
efficiency plots shortly ready
currents and HV trendings to be done
finalizing writing in the coming weeks
Conclusions
EEE meeting
26/04/2017
24