## Slide 1
Run 3 operation
(ITIS Galilei AREZZO)

## Slide 2
Run 3 operations and issues
Polarity change before the start of the RUN3 (10/2016)
Change of the gas flux chamber order: from “Bottom- Mid-Top” to “Top-Mid-Bottom” (6/2/2017)
End of SF6 (16/2/2017)
Voltage reduction (13/5/2017)

## Slide 3
Temperature and rate
During RUN2 it was observed a correlation between indoor temperature and rate
Not so good reconstruction parameters
MRPC3 found with half of the strips with inverted polarity
Intervention performed at the beginning of RUN3

## Slide 4
Channel distribution before polarity change in MRPC3 with correspondent Chi2 plot

## Slide 5
MRPC3 current vs temperature
F(x) = 0,1 x +0,97

## Slide 6
Arezzo, 16 marzo 2017
Rate in function of temperature
F(x) = 0,78 x + 27,75

## Slide 7
After the intervention
There is a decise improvement in the reconstruction parameters
During RUN3 it is still present a correlation between indoor temperature and rate
Is it possible that a gas flux problem is the cause?

## Slide 8
Channel distribution in MRPC3 with correspondent Chi2 plot after polarity change

## Slide 9
Leak search
Students using a leakseeker to discover possible leakage of MRPC
2 leaks in MRPC3
1 leak in MRPC1
Small leaks in MRPC2
Inversion of the flux line in order to place
the leaking chamber in first position

## Slide 10
Flux Chamber Inversion
Changing their order in the flux line

## Slide 11
After flux chamber inversion

## Slide 12
After the flux inversion
After the inversion, a small correlation between indoor temperature and rate has been found
Waiting to return to normal operation (re-sealing operation performed few days ago).

## Slide 13
SF6 End

## Slide 14
SF6 End
Sharp increase in rate of the events

## Slide 15
SF6 End
Multiplicity before 16/2

## Slide 16
SF6 End
Multiplicity after 16/2

## Slide 17
SF6 End
Cluster Multiplicity ante 10/4

## Slide 18
SF6 End
Cluster multiplicity after 13/4

## Slide 19
SF6 end
File dimension increase (about 300%!)
Disk space problem

## Slide 20
Temporary Solution
HV voltage reduction (~400 V)
Strong reduction of clusters
Consequent file dimension reduction
Lower rate