## Slide 1
The EEE network: central data management and student activities
Edoardo Bossini
Centro Fermi and INFN-Pisa
(on behalf of the EEE collaboration)
Padova, 30 Settembre 2016
1

## Slide 2
The Extreme Energy Events (EEE) project is a special experiment of Centro Studi e Ricerche Enrico Fermi (Roma) in collaboration with CERN, INFN and MIUR, focused on the study of high energy cosmic rays, carried out with the decisive contribution of students and teachers from high schools.
A large network of cosmic ray telescopes is deployed on the Italian territory. Students participate in the construction, maintenance and data analysis of the telescopes.
Synchronization within stations is performed through GPS system. The network is able to identify and study high energy cosmic rays (>1011 eV).
Mappa dei telescopi in funzione o in installazione
The EEE project

## Slide 3
PISA-01 telescope

## Slide 4
3 Multi-Gap Resistive Plate Chambers , with active surface of ~168x80 cm², readout by 24 longitudinal strips
Each side of the chamber host two front-end card, for signals discrimination and digitization
Particle longitudinal coordinate is extrapolated measuring the difference of the signal arrival time between the two edges, using Time to Digital Converter with <100 ps resolution
The telescope
X axis
y axis

## Slide 5
Not only tracking
Weather station:
Temperature (int., ext.)
Humidity
Pressure
Change in chamber efficiency
Impact on the muon flux (pressure)
GPS system (Spectracom TSynch)
can provide a event timestamp with a resolution 80 ns, synchronizing different stations.
Search for extended showers!

## Slide 6
80 high schools are currently involved in the project.
47 telescopes are already fully operational and took data during the Run 2 (October 2015-May 2016)
Need for a centralized data collection center :
Common (expert) analysis
Data Quality monitor
Redistribution to schools
Network size

## Slide 7
Network size
Data Reconstruction
Data quality monitoring
Database of analyzed files (with analysis relevant information)
Web services

## Slide 8
Online DQM
Single file
analysis
Trend, daily summary

## Slide 9
DQM monitor
Rate of candidate
tracks
Reconstruction efficiency
Time distribution
Fit

## Slide 10
Trend monitor
1
Track data are available in root format
Trending can be downloaded in csv format
File can be used for students (and expert) analysis, but first…

## Slide 11
Shift
Each school performs a daily check on the instrumentation and the data are reported on the dedicated logbook.
Students become our eyes!
And
more!

## Slide 12
Master class
Each school can develop its own analysis, but we give periodic master classes:
Shower simulation
Coincidence search
Forbush decrease
Telescope maintenance and dqm
Ground muon distribution of a ev proton shower simulated with «corsica»
Shower particle profile

## Slide 13
Master class
Arrival time difference between LAQU-01 and LAQU-02 stations
EEE (after pressure correction) Vs Oulu neutron monitor observatory
time
% variation
Pressure correction
Data comparison with international observatory

## Slide 14
Master class
Arrival time difference between LAQU-01 and LAQU-02 stations.
Entries
Arrival time difference [msec]
Concept of background and statistics must be carefully introduced!

## Slide 15
Conclusion
The EEE project is designed to combine scientific research and outreach
Students actively construct, maintain and perform data analysis of the detectors with outstanding enthusiasm
They can also take part in detector test and characterization, having a deeper overview of the research process
The introduction to the analysis is done through master classes on several topics. Main concept as background and calibration are given.
Many other talk has been presented during the congress!!