## Slide 1
Detector Simulation Working Group (DeSi-WG)
EEE telescope simulation
M.Battaglieri, S.Grazzi G.Mandaglio, C.Pellegrino, S.Pisano
September 2018
F.Coccetti, F.Noferini, M.Ungaro

## Slide 2
EEE MRPC/Telescope Geometry
EEE MRPC response
EEE Telescope response
Location
GEMC
CORSIKA
RecSw
Data
Physics analysis
DEtectorSImulation-WG
Goal: generate pseudo data using GEANT4 to track CORSIKA generated particle

## Slide 3
EEE MRPC response to cosmic rays implementation in GEANT4
DeSi-WG: targets and work plan
  MRPC geometry: material, size, …
  MRPC response (parametrized)
  Telescope response: geometry, trigger, …
  Telescope location: effect of roof, walls, surrounding materials, …
  Telescope: muon rates for different multiplicities
  Multi-telescopes: coincidence rates
  Single/multiple telescope(s) studies: bottom-up muons, …

## Slide 4
GEant4 Monte Carlo: GEMC
M.Ungaro
Realistic detector simulation
GEMC
A GEANT4 librarys based simulation tools
components description
components interaction
user-defined geometry and hit
internal generator (included cosmic rays)
multiple input/output format
CAD geometry accepted
interactive/batch mode
source on GitHub
GEMC graphic interface
Installed (and now working!) in EEE cluster at CNAF!

## Slide 5
EEE-MRPC simulation: geometry
Detailed drawings provided by R.Zuyeuski
Geometry/materials verified during assembly of Genova telescope at CERN (March 2017)

## Slide 6
EEE-MRPC simulation: geometry
Realistic geometry implemented in GEMC
materials (Al, Vetronite-G10, Cu, glass, Al-honeycomb, Gas
geometry
active layers (so far only bottom strips + gaps)

## Slide 7
EEE-MRPC simulation: response
No avalanche simulated in details
Effective hit process:
Sample XY (and Z) muon hit on on bottom strip plane
Assume both strips and gaps are active
Apply a spread of σ=8.4mm (2σ) to account for multiple hits and spread position resolution both in X and Y
Apply a time spread (constant) σ=94ps
MRPC parameters
90x160 active area
Active: 2.5cm x 24 strips + 0.7cm x (24-1) gaps
Time spread: σ = 94ps
  Cluster size: σX = 8.4 mm
  Cluster size: σY = 8.4 mm
  HITXY is gaussian-spread and projected on the sensitive area to derive strip multiplicity
  strip
  muon
  cluster
Resolution disuniformity not implemented yet
Nuclear Instruments and Methods in Physics Research A 593 (2008) 263– 268

## Slide 8
EEE-Telescope simulation: geometry
Telescope Parameters
3 chambers
-50/0/+50 cm apart
placed in a concrete box wall on all sides (30cm concrete)
Xhit
Yhit
XvsYhit
Multhit
Top
Mid
Bottom
￼
Individual response to cosmic muons (2-10 GeV) of the three chambers

## Slide 9
EEE-Telescope simulation: response
￼
Comparison to data
EEE Report: Description of the event reconstruction procedures for the EEE telescopes
  TOF
  Θ
  Φ
  DATA
  GEMC simulations

## Slide 10
EEE-Telescope simulation: response to cosmic
￼
Energy | fraction of the spectrum (%) | Rate 1248.8Hz * Rec/Gen | Rate -50cm/0/+50cm
0.2 - 2 GeV | 44.5 | 60.1Hz | 26.8Hz
2- 10 GeV | 41 | 53.5Hz | 22.0Hz
10- 100 GeV | 14.2 | 38.7Hz | 5.5Hz
100 - 500 GeV | 0.3 |  | 
Tot | 100 |  | 54.3Hz
Current EEE-telescope geometry: -50/0/+50 cm apart
Rates are obtained summing up muons generated in different energy intervals
Values should be compared to Rate measured in a single-layer-roof EEE telescope
Concrete vault
Muons gnerated on a sphere but with an uniform distribution on the plane
Absolute rate calculation

## Slide 11
Summary and future plans
EEE MRPC response implemented in GEANT4
EEE data reconstruction program modified to process pseudo-data
Simulations matches data angular and time distribution
Absolute rates of single muon hits on the telescope (3 chambers) are comparable
Fine-tuning of the simulations parameter (cluster size, time resolution, …) in progress
Next steps:
    use of CORSIKA to generate and propagate multi-muon hits (primary hadron in high atmosphere + shower propagation to the sea-level)
    Sim/data for multi-telescopes correlation comparison