## Slide 1
Introduzione al DQM
D. De Gruttola
Centro Fermi Roma
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018

## Slide 2
Summary
basis for a good data taking
EEE Data Quality Monitor (DQM)
main quantities to be monitored
data and tools to analyze them
2
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018

## Slide 3
3
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
Data Taking and Data Quality Monitor (DQM)
effective data taking period (duty cycle) needs to be the highest possible
costant acquisition to perform several measurements (a few examples here)
data taking and DQM are crucial
each school has the needed tools to:
access DQM
check the correct behavior of the
telescope
perform data analysis to study performance and physics phenomena

## Slide 4
4
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
24 copper strips to pick up the signal
trigger: six-fold coincidence (two chamber sides and three chambers)
x
y
- X coordinate determined by the fired strip
- Y coordinate obtained by measuring the time difference between the signals on the two sides of the chamber
x
y
Position of the hits

## Slide 5
DQM and quantities to be monitored
5
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018

## Slide 6
!!! each member of the Collaboration can monitor and analyze data from all the EEE telescopes !!!
Data Quality Monitor
https://iatw.cnaf.infn.it/eee/monitor/
6
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018

## Slide 7
information on the last run transferred to CNAF are given per each school
the status of a school is GREEN if there is a transfer in the last 3 hours, with reasonable paramaters of the run (rate, fraction of reconstructed tracks, …)
links to check the data quality, by means of DQM plots, are given per each telescope
DQM home page
v
v
v
https://iatw.cnaf.infn.it/eee/monitor/
online global monitor of all sites of the project
7
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
number of
collected tracks

## Slide 8
8
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
link to transfer history
list of daily reports from DQM
link to quantities to be monitored
trigger rate
reconstructed
tracks rate
https://iatw.cnaf.infn.it/eee/monitor/
DQM home page

## Slide 9
9
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
Telescopes acceptance
a tracking algorithm reconstructs trakcs crossing the telescope, by using the hits on each chamber
DQM is a basic tool to monitor the quality of the data taking
many quantities can be monitored online:
track lenght
Time of flight
angular distributiond
track quality (c2)
multiplicity
trigger rate , rate of events with hits, rate of events with good tracks

## Slide 10
DQM: rate, pressure and temperature
Daily report of rate, pressure and temperature
click
immediate detecting:
noisy periods
telescope inactivity
high trigger rate
low reconstruction efficiency
Important temperature fluctuations
pressure fluttuations
useful to find good periods to get barometric corrections
immediate detecting:
10
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018

## Slide 11
11
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
history rate, pressure and temperature monitor
click
DQM: rate, pressure and temperature

## Slide 12
12
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
DQM: histograms and alarms
histograms and alarms automatically produced by DQM
click

## Slide 13
13
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
DQM: multiplicity
noisy
events
single hit
cluster
hit multipliciity
cluster multipliciity
constant monitoring of event multiplicity
need of interventions on the telescope in case
the multiplicity is peaked at high values
expected
multiplicity

## Slide 14
χ2 tracks distribution
χ2 measures the shift of the track wrt hits
randomly aligned hits
and tracks of scattered particles:
tracks with high χ2
tracks with 1< χ2 < 10: particle candidates
DQM: tracks and χ2
global measurement
14
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018

## Slide 15
trending (measurement vs time)
rate of good tracks,
i.e. with χ2 < 10
rate of events with at least one good track
DQM: tracks and χ2
15
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018

## Slide 16
16
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
delta time distribution
between two consecutive trigger events

slope inversely proportional to trigger rate
DQM: time difference between two events
y = e-RDT
R = rate  1/R = mean

## Slide 17
angular distributions: azimuthal and polar angle
DQM: angular distributions
Azimuthal distribution
(bigger acceptance in the corners)
Polar distribution
(affected by telescope acceptance)
17
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018

## Slide 18
distributions of time of flight (TOF) and track lenght
distance between chambers 1 and 3
TOF ~ 3.3 ns  d= 1m
(d = distanza tra le camere)
DQM: time of flight and track lenght
tilted
tracks
18
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018

## Slide 19
19
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
DQM: file csv per analisi dati
download dei file dati:
csv header  summary for one run
cdv trending  trending of measured quantities
csv weather  temperature and pressure
Data collected in csv (comma separated values) files
They can be analised in Excel

## Slide 20
20
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
DQM: file root per analisi dati
Data are also collected as root files
root is a framework written in c++

## Slide 21
21
D. De Gruttola – EEE Run Coordination Meeting open to schools
24/10/2018
It is possible to retrieve some data from several runs by using the elog
Real data and MC data are available
This tool has been used for ICD 2017
Cut to have good tracks
Chose a telescope
Chose date
(no more than 2 or 3 days)
Please check output dimensions before asking many days and have too big files
Tip it if you want MC data
E-log: data query

## Slide 22
Back up

## Slide 23
Team Viewer and Data Taking
controllo tensioni
monitoraggio T e p
acquisizione
!!! remote control of all the telescopes is always possible!!!

## Slide 24
multeplicity of 24
channels of a single FEA
possibility to check
the correct behavior
of each single channel
and identify dead or
noisy channels
Strip multiplicity

## Slide 25
molteplicity of triggered
events
number of strips giving
a signal in each event
the distribuzione has to
be peaked at 1
Event multiplicity

## Slide 26
Analysis example
dependence of rate from temperature and pressure(lecture from I. Gnesi, 16 April)
effect of solar flares on the cosmic ray flux (lecture from I. Gnesi, 16 April)

## Slide 27
Barometric corrections
didactic experiments on cosmic rays
measurement with Geiger counters
and scintillators
measurement of the
barometric effect
pressure variations affect the secondary cosmic ray flux according to the law:
DI = -bDp
atmospheric pressure
yield corrected by pressure
muon yield

## Slide 28
atmospheric pressure is a direct measurement of the amount of air to be crossed by a shower before reaching the telescope
pressure variations cause variations in the particle flux measured by the telescope
Barometric corrections

## Slide 29
pressure can be read
by weather station (if possible)
by siti di rilevamento nelle vicinanze
Pressure monitoring

## Slide 30
if mean multiplicity greater than 2, an intervention is needed: need to tune the chamber voltage or the internal temperature
ottobre
luglio
Bad behavior

## Slide 31
once the flux is corrected by atmospheric pressure physics observables become visible
Cosmic Ray Flux Decrease
day/night modulation
+
thermal drift
Barometric corrections

## Slide 32
DQM: csv files for data analysis
download of data files:
csv header  summary of run information
cdv trending  quantities vs time
csv weather  data of temperature and pressure
data are collected in csv files (comma separated values)
and can be analyszed by Excel

## Slide 33
data are collected also in root files
root is a framework written in c++
DQM: root files for data analysis